## Slide 1: Replacing laboratory hardware with integrated electronics for motor control
Conclusion (Arial Bold
1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Group 01.03: Asger Kühl, Berk Gezer, Frederik Ettrup Larsen, Irene Danvy
Introduction
The DTU Roadrunner team is seeking to replace an important motor control component in the ecocar.
DTU roadrunners is participating in the Shell Eco marathon, and due to a rule change, power consumption is now counted to determine the fuel efficiency of the car.
Combining this with a goal to reduce the overall weight of the car, this project focuses on replacing a very power consuming component, the National Instrumets Reconfigurable I/O (RIO), with our own integrated electronics.
Abstract: In this project we have done... These things
Power savings
Due to a rule change in the competition, one of our goals is to make the system use less power.
The main power saving is done by the replacement itself, as the integrated electronics is very barebone and therefore does no unneeded operations. A comparison between the power usage of the two systems can be seen on figure 1
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Mellemrubrik (Arial Bold
1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Indsæt billede
Billedtekst (Arial Regular 15/24Pt.)
Billedtekst (Arial Regular 15/24Pt.)
Indsæt billede
Billedtekst (Arial Regular 15/24Pt.)
Due to a rule change in the competition[1], one of our goals is to make the system use less power.
The main power saving is done by the replacement itself, as the integrated electronics is very barebone and therefore does no unneeded operations. A comparison between the power usage of the two systems can be seen on figure 1.
[1] Make sure we talk about this elsewhere, or rephrase it here
Due to a rule change in the competition[1], one of our goals is to make the system use less power.
The main power saving is done by the replacement itself, as the integrated electronics is very barebone and therefore does no unneeded operations. A comparison between the power usage of the two systems can be seen on figure 1.
[1] Make sure we talk about this elsewhere, or rephrase it here

## Slide 2: Titel (3 varianter Arial Bold 1. 100/120pt, 2. 160/170pt, 3. 200/220pt. )
Mellemrubrik (Arial Bold
1. 18/24pt. el.
2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Forfatter: Navn, Titel (Arial Bold 60/100pt)
Mellemrubrik (Arial Bold
1. 18/24pt. el.
2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Manchet (Arial Bold 1. 35/45pt. el. 2. 48/60pt)
Mellemrubrik (Arial Bold
1. 18/24pt. el.
2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Mellemrubrik (Arial Bold
1. 18/24pt. el.
2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Notes: Tekst og Streger i 100% farve – Baggrund i 90% Transparent.

## Slide 3: Titel (3 varianter Arial Bold 1. 100/120pt, 2. 160/170pt, 3. 200/220pt. )
Indsæt billede
Mellemrubrik (Arial Bold
1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Group 01.03: Asger Kühl, Berk Gezer, Frederik Ettrup Larsen, Irene Danvy
Introduction
The DTU Roadrunner team is seeking to replace an important motor control component in the ecocar.
DTU roadrunners is participating in the Shell Eco marathon, and due to a rule change, power consumption is now counted to determine the fuel efficiency of the car.
Combining this with a goal to reduce the overall weight of the car, this project focuses on replacing a very power consuming component, the National Instrumets Reconfigurable I/O (RIO), with our own integrated electronics.
Abstract: In this paper we will discuss how we lessened the power consumption of the fuel efficient 'EcoCar' built by DTU Roadrunners to participate in the annual Shell EcoMarathon competition. For the first time this year, the competition takes electrical energy used into account, an aspect of the EcoCar which hasn't been optimized at all. The component in the car which consistently consumes the most power is the motor control unit currently a National Instruments reprogrammable I/O, shortened 'RIO’. Our approach to lowering the EcoCar's power consumption was therefore to replace the RIO with our own embedded electronics, without losing any functionality. The embedded electronics was made using only one microcontroller, and removed no functionalities of the car. This resulted in the power consumption being lowered considerably, making the car more ecofriendly and therefore more eligible to win the EcoMarathon.
Power savings
Due to a rule change in the competition, one of our goals is to make the system use less power.
The main power saving is done by the replacement itself, as the integrated electronics is very barebone and therefore does no unneeded operations. A comparison between the power usage of the two systems can be seen on figure 3
Mellemrubrik (Arial Bold
1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Indsæt billede
Billedtekst (Arial Regular 15/24Pt.)
Billedtekst (Arial Regular 15/24Pt.)
Fig. 3 The current into the RIO and the ECU over time

## Slide 4: Titel (3 varianter Arial Bold 1. 100/120pt, 2. 160/170pt, 3. 200/220pt. )
Forfatter: Navn, Titel (Arial Bold 60/100pt)
Mellemrubrik (Arial Bold
1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Indsæt billede
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Brødtekst (Arial 1. 18/24pt. el. 2. 35/45pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)
Note eller Institutnavn (Arial Regular 18/24pt.)